## Slide 1: Introduction to Spatial Computing CSE 555
Fundamental Spatial Concepts
Some slides adapted from Worboys and Duckham (2004) GIS: A Computing Perspective, Second Edition, CRC Press

## Slide 2: Logical Data Model for Spatial Data

## Slide 3: Two Types of Models
Field-based model:
  Contains a function from a spatial framework to an attribute domain
  Patterns of topographic altitudes, rainfall, etc.
Object-based model:
  treats the space as populated by discrete, identifiable entities each with a geospatial reference
  Buildings, roads, etc.

## Slide 4: Sample Raw Data
Tuples recording annual weather conditions at different locations
  The field-based and object-based approaches are attempts to impose structure and pattern on such data.

## Slide 5: Field-based approach
Treats information as a collection of fields
  Each field defines the spatial variation of an attribute as a function from the set of locations to an attribute domain

## Slide 6: Object-based Approach
Clumps a relation as single or groups of tuples
  Certain groups of measurements of climatic variables can be grouped together into a finite set of types

## Slide 7: Field Based Models

## Slide 8: Spatial Framework
Spatial framework: a partition of a region of space, forming a finite tessellation of spatial objects
In the plane, the elements of a spatial framework are polygons
Must be a finite structure for computational purposes
Often the application domain will not be finite and sampling is necessary.
Imprecision is introduced by the sampling process.

## Slide 9: Spatial Fields
If the spatial framework is a Euclidean plane and the attribute domain is a subset of the set of real numbers;
  The Euclidean plane plays the role of the horizontal xy-plane
  The spatial field values give the z-coordinates, or “heights” above the plane
  Field Functions:
f: Spatial Framework  Attribute Domain

## Slide 10: Layers in a GIS
Can be considered as a the combination of the spatial framework and the field that assigns values for each location in the framework
  There may be many layers in a spatial database

## Slide 11: Properties of Attribute Domain
The attribute domain may contain values which are commonly classified into four levels of measurement
  Nominal attribute: simple labels; qualitative; cannot be ordered; and arithmetic operators are not permissible
  Ordinal attribute: ordered labels; qualitative; and cannot be subjected to arithmetic operators, apart from ordering
  Interval attributes: quantities on a scale without any fixed point; can be compared for size, with the magnitude of the difference being meaningful; the ratio of two interval attributes values is not meaningful
  Ratio attributes: quantities on a scale with respect to a fixed point; can support a wide range of arithmetical operations, including addition, subtraction, multiplication, and division

## Slide 12: Continuous and differentiable fields
Continuous field: small changes in location leads to small changes in the corresponding attribute value
Differentiable field: rate of change (slope) is defined everywhere
Spatial framework and attribute domain must be continuous for both these types of fields
Every differentiable field must also be continuous, but not every continuous field is differentiable

## Slide 13: One dimensional examples
Fields may be plotted as a graph of attribute value against spatial framework
Continuous and differentiable; the slope of the curve can be defined at every point

## Slide 14: One dimensional examples
The field is continuous (the graph is connected) but not everywhere differentiable. There is an ambiguity in the slope, with two choices at the articulation point between the two straight line segments.
Continuous and not differentiable; the slope of the curve cannot be defined at one or more points

## Slide 15: One dimensional examples
The graph is not connected and so the field in not continuous and not differentiable.
Not Continuous and not differentiable;

## Slide 16: Two dimensional examples
The slope is dependent on the particular location and on the bearing at that location

## Slide 17: Operations on Fields
A field operation takes as input one or more fields and returns a resultant field
The system of possible operations on fields in a field-based model is referred to as map algebra
Three main classes of operations
  Local
  Focal
  Zonal

## Slide 18: Local Operations
Local operation: acts upon one or more spatial fields to produce a new field
The value of the new field at any location is dependent on the values of the input field function at that location.

## Slide 19: Neighborhood function
Given a spatial framework F, a neighborhood function n is a function that associates with each location x a set of locations that are “near” to x

## Slide 20: Focal Operations
Focal operation: the attribute value derived at a location x may depend on the attributes of the input spatial field functions at x and the attributes of these functions in the neighborhood n(x) of x

## Slide 21: Zonal Operations
Zonal operation: aggregates values of a field over a set of zones (arising in general from another field function) in the spatial framework
For each location x:
  Find the Zone Zi in which x is contained
  Compute the values of the field function f applied to each point in Zi
  Derive a single value ζ(x) of the new field from the values computed in step 2

## Slide 22: Question
Consider a spatial framework defined by latitudes and longitude (1 degree by 1 degree cells) to represent (time-average) annual temperatures for years 1900 to present over the surface of Earth. Zones should be defined accordingly. Assume that each cell belongs to a unique zone.
Classify following operations into local, focal, zonal, or a combination of these operations:
Determine warmest temperature (or year) for each cell.
Determine warmest cell in each country in year 2000.
Identify country with highest average cell temperature in year 2000.
For each cell, compute spatial-neighborhood average temperature in the year 2000.
For each cell, compute heat-island-factor as the difference between its temperature and its spatial-neighborhood average temperature for the year 2000. Assume the results of previous step were available as an input for this step.
Compute average annual temperature of surface of Earth for each year.

## Slide 23: Spatial Auto-Correlation
Spatial autocorrelation is a quantitative expression of Tobler’s first law of geography (1970)
  “Everything is related to everything else, but near things are more related than distant thing”
  Spatial autocorrelation measures the degree of clustering of values in a spatial field
If there is no apparent relationship between attribute value and location then there is zero spatial autocorrelation
If like values tend to cluster together, then the field exhibits high positive spatial autocorrelation
If like values tend to be located away from each other, then there is negative spatial autocorrelation

## Slide 24: Object Based Models

## Slide 25: Entities
Object-based models decompose an information space into objects or entities.
An entity must be:
  Identifiable
  Relevant (be of interest)
  Describable (have characteristics)
The frame of spatial reference is provided by the entities themselves.

## Slide 26: House Object
  Has several attributes, such as registration date, address, owner and boundary, which are themselves objects

## Slide 27: House Object
  The actual values of these attributes are literals
    If the house is registered to a new owner, we may change the registration attribute to a new date, however, the date November 5th, 1994” still exists as a date

## Slide 28: Spatial objects
Spatial objects are called “spatial” because they exist inside “space”, called the embedding space
A set of primitive objects can be specified.
Out of these all others in the application domain can be constructed, using an agreed set of operations
Point-line-polygon primitives are common in existing systems.

## Slide 29: GIS Analysis
Query: For Italy’s capital city, Rome, calculate the total length of the River Tiber which lies within 2.5 km of the Colosseum.
First we need to model the relevant parts as objects.
Operation length will act on arc, and intersect will apply to form the piece of the arc in common with the disc

## Slide 30: GIS Analysis
A process of discretization must convert the objects to types that are computationally tractable
A circle may be represented as a discrete polygonal area,
Arcs by chains of line segments,
Points may be embedded in some discrete space

## Slide 31: Hierarchy of Spatial object types
The most general spatial object type spatial is at the top of the hierarchy
Spatial type is the disjoint union of types point and extent
Class extent may be specialized by dimension into types 1- extent and 2- extent
Two sub types of the one dimensional extents are described as arc and loop, specializing to simple arc and simple loop when there are no self-crossings

## Slide 32: Hierarchy of Spatial object types
The fundamental areal object is area
A connected area is a region
A region that is simply connected (no holes) is a cell

## Slide 33: Topological Operators
Object types with an assumed underlying topology are point, arc, loop and area
Broadly three kinds Operations:
  (1) Topological:
  boundary, interior, closure and connected are defined in the usual manner
  is within provides a relationship between a point and a simple loop, returning true if the point is enclosed by the loop
  …… Many more are possible

## Slide 34: Topological Operators
Object types with an assumed underlying topology are point, arc, loop and area
Broadly three kinds Operations:
  (1) Set Oriented:
  E.g., Intersection, union, subset of, etc.
(2) Euclidian:
  E.g., distance, length, perimeter, centroid, etc.

## Slide 35: Topological Spatial Operations for areas
  X meets Y if X and Y touch externally in a common portion of their boundaries
  X overlaps Y if X and Y impinge into each other’s interiors

## Slide 36: Topological Spatial Operations for areas
  X is inside Y if X is a subset of Y and X, Y do not share a common portion of boundary
  X covers Y if Y is a subset of X and X, Y touch externally in a common portion of their boundaries

## Slide 37: A “common” framework for Topological Operators
Fundamental Relationships between X and Y |  |  |  | 
boundary(X) boundary(Y) | Interior(X) interior(Y) | boundary(X) Interior(Y) | Interior(X) boundary(Y) | Interpretation
1 | 0 | 0 | 0 | Meets
1 | 1 | 1 | 1 | Overlaps
0 | 1 | 1 | 0 | X inside Y
… | …. | …. | …. | ….
… | …. | …. | …. | ….
… | …. | …. | …. | ….
Fundamental Relationships between X and Y |  |  |  | 
 |  |  |  | Interpretation
1 | 0 | 0 | 0 | Meets
1 | 1 | 1 | 1 | Overlaps
0 | 1 | 1 | 0 | X inside Y
… | …. | …. | …. | ….
… | …. | …. | …. | ….
… | …. | …. | …. | ….
Fill this table and provide interpretations in the right column

## Slide 38: A “common” framework for Topological Operators
Fundamental Relationships between X and Y |  |  |  | 
boundary(X) boundary(Y) | Interior(X) interior(Y) | boundary(X) Interior(Y) | Interior(X) boundary(Y) | Interpretation
… | …. | …. | …. | ….
… | …. | …. | …. | ….
… | …. | …. | …. | ….
… | …. | …. | …. | ….
… | …. | …. | …. | ….
… | …. | …. | …. | ….
Fundamental Relationships between X and Y |  |  |  | 
 |  |  |  | Interpretation
… | …. | …. | …. | ….
… | …. | …. | …. | ….
… | …. | …. | …. | ….
… | …. | …. | …. | ….
… | …. | …. | …. | ….
… | …. | …. | …. | ….
These can be considered as a rough equivalent to relational operators used to model relational queries.

## Slide 39: Nine intersection model of Topological Relationships
Many toplogical Relationship between A and B can be
  specified using 9 intersection model
  Examples on next slide
Nine intersections
  intersections between interior, boundary, exterior of A, B
  A and B are spatial objects in a two dimensional plane.
  Can be arranged as a 3 by 3 matrix
  Matrix element take a value of 0 (false) or 1 (true).

## Slide 40: Nine intersection model of Topological Relationships